## Slide 1: Irrigation Efficiency on small farms and gardens.
Dean Moberg
USDA – NRCS
Notes: Materials:
-sponge
-bucket
-tub
-food color
-three pint mason jars labeled >FC, easy, hard

## Slide 2: Welcome and introductions
Monet, Haystacks
Notes: What is NRCS?
Who is here?
How many commercial farmers?
How many gardeners?
Others?
Vegetables?
Fruits and berries?
Pasture?
Other?
Organic?

## Slide 3: Irrigation as a system
Plants.
Soil.
Hardware.
Escher, Waterfall

## Slide 4: Irrigation as a system
Plants.
Soil.
Hardware.

## Slide 5
https://catalog.extension.oregonstate.edu/em8713
Notes: This website has links to concise two-page guides to irrigating many crops commonly grown in the Willamette Valley. It is available for purchase but not available free online.

## Slide 6
Hess et al., 1997
Notes: The guide for blueberries.
Hess, Mario; B. Strik, J. Smesrud, and J. Selker
Western Oregon Blueberry Irrigation Guide
OSU: 1997

## Slide 7: Evapotranspiration (ET)
Peak ET for blueberries = 0.26 in/day
Notes: Enlargement of the graph for blueberries.
8 inches in July / 31 days = 0.26 inches/day

## Slide 8
Notes: Evapotranspiration (ET) values above tend to be high estimates (somewhat warmer than average days). On cool days, actual ET will be less. On very hot days, ET may be more.
Rooting depth is based on healthy crops without soil restrictions. For annual crops, of course, the root depth will be less early in the season.

## Slide 9
http://irrigation.wsu.edu/index.php
Notes: This website has tools to help calculate the amount of water your irrigation system supplies per hour.

## Slide 11
Notes: Nozzle diameter is usually stamped into the brass nozzle (not always easy to see). You can also use drill bits to measure the nozzle diameter. For rotator type sprinklers, you will need to consult your dealer or the manufacturer website.
Pressure is best measured with a pressure gauge and pitot tube. If you don’t have this, you can measure how many gallons come out of one sprinkler in one minute (use a short piece of scrap garden hose, a bucket, measuring cup and a watch). Then enter all other data with actual numbers and adjust the pressure until you match your gallons per minute.
Line spacing = distance between irrigation pipes.
Head spacing = distance between sprinklers along the pipe.
Sprinkler efficiency = 70% is a good value to use.

## Slide 12
Notes: 0.53 gph = 2 liters per hour

## Slide 13: Double drip calculation on widely spaced crops?
0.05 in/hr
0.10 in/hr
Notes: There is some healthy disagreement on how to measure distance between irrigation lines for widely spaced crops. When crops are closely spaced, like broccoli planted in 3 foot wide rows, there is typically one drip line per row and the spacing is 3 feet.
But for blueberries planted in 11 foot wide rows (like in previous example), with one drip line per row, there are two approaches:
1. Just figure 11 foot spacing, which is 0.05 in/hr.
2. Assume that ET rates are based on sprinkler irrigation and that half of the sprinkler water percolates down between the rows with no benefit to the crop. In this case, you can figure that for DRIP irrigation, the actual blueberry root zone is 5 feet wide and so the effective rate of blueberries is doubled.

## Slide 14
Notes: If your irrigation system does not fit one of the calculators, you can use the tuna can approach.

## Slide 15: Irrigation duration
Blueberries in July:
Average ET = 0.25 inches/day
Drip rate = 0.10 inches/hour
(0.25 inches/day) / (0.10 inches/hour)
= 2.5 hours /day
Notes: Remember that cool days will be less and very hot days may be more.

## Slide 16: Irrigation duration
2.5 hours /day, or
5.0 hours every two days, or
7.5 hours every three days, or
10 hours every four days, or
20 hours every eight days

## Slide 17: Problem
What if soil can’t hold that much water?
20 hours x 0.10 in/hour = 2.0 inches
Remember this number

## Slide 18: Irrigation as a system
Plants.
Soil.
Hardware.

## Slide 19: Soil / water, simplified
Smesrud et al., 1997
Notes: Clay holds more water, but sand has higher infiltration rate (can apply irrigation water faster).
But it would be helpful to quantify how much water a soil can hold.

## Slide 20
Notes: "The source of this material is the COMET® Website at http://meted.ucar.edu/ of the University Corporation for Atmospheric Research (UCAR), sponsored in part through cooperative agreement(s) with the National Oceanic and Atmospheric Administration (NOAA), U.S. Department of Commerce (DOC). ©1997-2016 University Corporation for Atmospheric Research. All Rights Reserved."

## Slide 21: Web Soil Survey
Free, fun, easy
http://websoilsurvey.sc.egov.usda.gov/App/HomePage.htm

## Slide 22
Notes: AWHC generated for 0-18 inch soil depth.
This is a field on the PCC Rock Creek campus.

## Slide 23
Notes: AWHC generated for 0-18 inch soil depth.
This is a field on the PCC Rock Creek campus.

## Slide 24: Volunteer needed
Notes: Demonstrate FC, MAD, PWP, AW using a sponge and dyed water, putting water into quart mason jars labeled >FC, “easy”, “hard”.
Click to next slide while doing demo.
> FC: Water drains by gravity out of large pores in sponge/soil
> MAD (“easy”): Gentle squeezing of sponge easily provides water.
< MAD (“hard”): Stronger squeezing of sponge also provides water; crop wilts during day but recovers at night.
PWP: Still water available, but crop no longer recovers at night and eventually dies.

## Slide 25: Available Water (percent)
Notes: The part of available water that is easily available to plants is called “Maximum Allowable Depletion” (MAD). For many crops, MAD = 50% of AW. MAD is not shown in this graph because MAD differs by crop.
Note that for silt loam:
FC = about 38 cm/m
PWP = about 18 cm/m
AW = about 20 cm/m (or 0.20 cm/cm as we saw in the web soil survey report).

## Slide 26: Available Water (percent)
Good soil health practices can increase this.
20%
Notes: Above FC ~10%
Easily available ~10%
More difficult ~10%
Not available to plants ~15-20%
BUT WE NEED TO KNOW WHAT THE MAD IS.
WE ALSO NEED TO KNOW HOW MANY INCHES OF WATER TO APPLY, NOT WHAT PERCENT. WHAT DO WE NEED TO KNOW TO CONVERT PERCENT TO INCHES OF MAD?

## Slide 27: From blueberry guide
Effective root depth = 18 inches
Maximum allowable depletion = 50%

## Slide 28: Maximum allowable depletion
10%
Notes: The part of available water that is easily available to plants is called “Maximum Allowable Depletion” (MAD). For many crops, MAD = 50% of AW. MAD is not shown in this graph because MAD differs by crop.
Note that for silt loam:
FC = about 38 cm/m
PWP = about 18 cm/m
AW = about 20 cm/m (or 0.20 cm/cm as we saw in the web soil survey report).

## Slide 29: Available water (inches)

## Slide 30: Total available water
Your available water calculation will depend on your soil and crop.

## Slide 31: Total available water
Can we apply 2.0 inches of water to this crop/soil combination?

## Slide 32
Notes: Going thru this paper form with pencil and calculator is instructive, but it’s a bit like doing your taxes with paper forms.
Many folks prefer to do their taxes on line now, and likewise irrigation water management is becoming an on line process.

## Slide 33
Notes: Going thru this paper form with pencil and calculator is instructive, but it’s a bit like doing your taxes with paper forms.
Many folks prefer to do their taxes on line now, and likewise irrigation water management is becoming an on line process.

## Slide 34
http://weather.wsu.edu/ism/index.php?m=1
Notes: WSU irrigation scheduler mobile

## Slide 39
Notes: Don’t apply water in excess of deficit.

## Slide 40
Notes: You can forecast precip and ET into the future.
Note that you can edit data on prior dates to add in irrigations that you didn’t record previously.
“Water use” (first column) = ET

## Slide 41
Notes: You need to determine how many inches of water you apply.

## Slide 42: Reality check – human hand
25-50% AWC
50-75% AWC
75-100% AWC
Typical silt loam shown
Notes: http://www.nrcs.usda.gov/wps/portal/nrcs/detail/wy/soils/?cid=nrcs142p2_026831
Because MAD for many crops is 50% AWC, the soil pictured at top left is dry enough that it is causing crop stress.
Silt loam
25-50%: ball forms, dry crumbs break off
50-75%: ball forms, no crumbs break off
75-100%: ball forms, moisture is on fingers

## Slide 43: What’s next
Talk about hardware?
Or answer your questions?

## Slide 44: Irrigation as a system
Hardware.
Soil.
Plants.

## Slide 45: Hardware
Flood
Sprinkler
Micro
Notes: This presentation will touch on hardware but the goal is not to teach folks to design systems as that is complicated and is usually done by vendors.

## Slide 46: Hardware
Flood
Sprinkler
Micro

## Slide 47: Sprinkler benefits
Can be portable
Cooling
Frost protection
Notes: Impact sprinklers typically deliver more gpm at a wider spacing, benefit: need fewer per acre.
Rotator sprinkler benefits: high uniformity, no tools needed to install, better shields (keeping water off road, etc.)

## Slide 48: Sprinkler drawbacks
Uniformity difficult
Affected by wind
Wet foliage
High energy cost
Smaller sets
Scott and Cory, 1957
Notes: Scott, Verne H and J. A. Cory, Sprinkler and Lateral Spacing, California Agriculture 1957.
Uniformity coefficient of 80% considered minimum

## Slide 49: Sprinkler tip 1: professional design
Pump pressure and flow
Pipeline water velocity, flow, pressure
Sprinkler type and spacing
Air, vacuum release, drain valves
Thrust blocks

## Slide 50: Sprinkler tip 2: overlap

## Slide 51: Sprinkler tip 3: pressure
Smesrud et al., 1997
Low
Correct
Notes: Smesrud, Jason, Mario Hess and John Selker
Western Oregon Irrigation Guides: Background and References
OSU: 1997

## Slide 52: Sprinkler tip 4: maintenance

## Slide 53: Sprinkler tip 4: water hammer

## Slide 54: Micro (drip) benefits
Less waste
Uniform
Low labor
Dry foliage
Less bacteria on fruit?

## Slide 55: Micro drawbacks
Hard to see clogs and leaks
Animal damage
Hard to “catch up”

## Slide 56: Micro tip 1: good filtration

## Slide 57: Micro tip 2: regular flush
Notes: Frequency depends on quality of water.
Municipal water: beginning, middle and end of season
Stream water: weekly might be needed.

## Slide 58: Staying legal
Water rights specify how you may irrigate:
    Rate (gallons per minute)
    Total amount (inches per year)
    Dates
See watermaster for help:
    1400 SW Walnut St, Suite 240 Hillsboro, Oregon 97123

## Slide 59: And justice for all
The U.S. Department of Agriculture (USDA) prohibits discrimination against its customers, employees and applicants for employment on the bases of race, color, national origin, age, disability, sex, gender
identity, religion, reprisal, and where applicable, political beliefs, marital status, familial or parental status, sexual orientation, or all or part of an individual’s income is derived from any public assistance
program, or protected genetic information in employment or in any program or activity conducted or funded by the Department. (Not all prohibited bases apply to all programs and/or employment
activities.)
Vonnoh, Coquelicots

## Slide 60: And justice for all
The U.S. Department of Agriculture (USDA) prohibits discrimination against its customers, employees and applicants for employment on the bases of race, color, national origin, age, disability, sex, gender
identity, religion, reprisal, and where applicable, political beliefs, marital status, familial or parental status, sexual orientation, or all or part of an individual’s income is derived from any public assistance
program, or protected genetic information in employment or in any program or activity conducted or funded by the Department. (Not all prohibited bases apply to all programs and/or employment
activities.)

## Slide 61: Questions?

## Slide 62: Rooting depth
SCS, 1991
Notes: Maximum root depths can be quite high:
Tomato and lettuce = 5-8 feet deep
So, use ¼ or ½ of maximum root depth to estimate root zone that is really suitable for AW calculations.
SCS, National Engineering Handbook Section 15: Irrigation. 1991.